## Slide 1: Embedded System Design(EEL 7150) PROJECT
KARAN BHAKUNI - M22RM003
RAHUL MADAAN – M22RM008
Course Instructor : Dr. Deepak Fulwani

## Slide 2
ADAPTIVE BRIGHTNESS CONTROL USING LDR(Light Dependent Resistor) SENSOR
ON STM32F412 NUCELO BOARD

## Slide 3: HOME APPLIANCES
Ref: Wikipedia images

## Slide 4: Intensity Based:
Ambient light sensor
Ref: Wikipedia images

## Slide 5: Circuit Diagram

## Slide 6: SETUP

## Slide 7: Method-1
Configuring the Clocks and MODER register
Initializing the Header file
While(1)
If voltage is detected
LED ON
LED OFF
Y
N

## Slide 9: Method-2
num_steps = FADE_TIME / DELAY_TIME; calculates the number of fade steps required to complete the entire fade duration. In this case, num_steps would be 100
step_delay = FADE_TIME / num_steps; calculates the duration of each fade step. In this case, step_delay would be 20
If voltage is detected
for (int i = 0; i < num_steps; i++)
Y
duty_cycle = ((i + 1) * 100) / num_steps;
delay = duty_cycle * step_delay / 100
off_delay = step_delay - delay
LED ON
LED OFF

## Slide 11
Method-3
Configuring the Clocks (ADC1)and MODER register
Enable continuous conversion mode, EOC after each conversion ,enable ADC conversion in regular sequence
Initializing the Header file
While(1)
Checking until conversion completes
if((ADC1->SR & (0x2)))
clear the status register
starting conversion by SWSTART

## Slide 12
While(1)
Checking until conversion completes
if((ADC1->SR & (0x2)))
clear the status register
starting conversion by SWSTART
duty_cycle=adc_value/80
delay = duty_cycle
off_delay = 100 - delay
LED ON
LED OFF

## Slide 14: Improvements and Future Work
1.We can also integrate LDR sensor with Analog Output and directly map it to change brightness of LED.
2. We can also integrate LCD screen to show the brightness percentage on it.

## Slide 15: References
1.Datasheet, Reference Manual and Board Schematic of STM32F412 nucleo board.
2.Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C. By Dr. Yifeng Zhu.

## Slide 16
THANK YOU!
Any Questions?